## Slide 1: Arriga Plains Bore Monitoring Project
Brian Prove
Mitchell River Watershed Management Group

## Slide 2: Aims
Carry out bore monitoring and sampling in 2017 and 2018
Compare these results to those obtained by Qld DNR
To inform the farmers and landholders in the area of the information gained
To determine any management/mitigation strategies require to manage and live with the situation

## Slide 3: INTRODUCTION AND Background
Bores in the Arriga Plains area were monitored by Qld Dept of Natural Resources from 2000 to 2010

## Slide 4: Acknowledgements
Mitchell River Watershed Management Group
Australian Government for funding via LandCare
Farmers and landholders who allowed access to their properties to find the bores and sample them
David Morrison and Tracey Whitling, Qld Dept of Natural Resources
Drewe Burgess Canegrowers Mareeba

## Slide 5: Methods
Locate all DNR bores and private bores
Measure the depth to the water table with a tape measure and plopper.
Obtain a sample of water from 30cm below the water surface
Measure with a probe electrical conductivity
187 bores, 91were not located and/or damaged

## Slide 6: Bore Locations in the Catchment

## Slide 7: Watertable Depth Dec 2017 and Oct 2018

## Slide 8: Salinity levels
 | Conductivity (uS/cm) | 
Good drinking water | 0-800 | 
Upper limit for drinking | 800-2500 | Care with irrigation
Brackish | 2,500-10,000 | Not suitable for irrigation
Seawater | 10,000-50,000 | Corrosion
Brine | >50,000 | 

## Slide 9: Conductivity Dec 2017 and Oct 2018

## Slide 10: Groundwater and Conductivity 2010

## Slide 11: Groundwater Risk 2010

## Slide 12: 2010 Water Quality Summary

## Slide 13: Salinity levels
 | Conductivity (uS/cm) | 
Good drinking water | 0-800 | 
Upper limit for drinking | 800-2500 | Care with irrigation
Brackish | 2,500-10,000 | Not suitable for irrigation
Seawater | 10,000-50,000 | Corrosion
Brine | >50,000 | 

## Slide 14: Changes from 2010 to 2017-18
Average rise in watertable height of between 0.2 and 0.5 mteres
No overall change in conductivity or slight decrease
Reasons – dry period for latest monitoring, dewatering by landholders?

## Slide 15: Background Rainfall Data Mareeba A’port

## Slide 16: Whats next?
Ongoing management and monitoring by who?
Landholders and farmers!
Bores for dewatering noting the need for careful use of saline water
Planting of selective trees in key areas (recharge and high water table areas)
Others

## Slide 17: Thank you Any questions